## Slide 1: BMWG – Containerized Infrastructure Benchmarking
IETF 111
July 19-23, 2020
Online

## Slide 2: Hackathon Plan
The main goal is to figure out container networking performance impacts by various resource options.
  Related Draft: Considerations for Benchmarking Network Performance in Containerized Infrastructures ​https://tools.ietf.org/html/draft-dcn-bmwg-containerized-infra
  Two main features
    Implementing containerized infrastructure with various network models
    Verifying performance impacts depending on configuration settings

## Slide 3: Hackathon Plan
Plan for Hackathon-110

## Slide 4: What got done
Discussion for draft update
  Need to clear definition and description of container networking
Gathering benchmarking experience done by other communities (ViNePERF in Anuket, userspace-cni, Intel, ..)
Re-Classification of network model
  From vSwitch aspect

## Slide 5: What got done
Benchmarking Scenario - Networking Acceleration
OVS-DPDK / VPP
Traffic Generator (T-Rex)
Port
Port
NIC
Port
Port
OVS-DPDK/VPP
Kernel
PMD
vhost-user
vhost-user
C-VNF
virtio-user
virtio-user
SR-IOV
Traffic Generator (T-Rex)
Port
Port
SR-IOV NIC
Port
Port
Kernel
C-VNF
VF
VF
VF driver
VF driver
* In both case, Multus CNI plugin is needed to create multiple interface of VNF
* For SR-IOV scenario, SR-IOV plugin in DPDK mode is needed to create VF driver of VNF
* C-VNF : L2fwd

## Slide 6: What got done
Benchmarking Scenario – NUMA Affinity
NIC & vSwitch on same NUMA node
NIC & vSwitch on difference NUMA node
* This scenarios are based on “Cross-NUMA test” case in ViNePERF from Anuket project (OPNFV vsperf in previous)
With OVS-DPDK / VPP, we compare network performance with different NUMA zone
Scenario1 (s1)
Scenario2 (s2)
Scenario4 (s4)
Scenario3 (s3)

## Slide 7: What got done
Benchmarking Configuration
Hardware
CPU | Intel(R) Xeon(R) Gold 5220R CPU @ 2.20GHz 48 CPU cores * 2 NUMA nodes
Memory | 256GB: 32GB x 4DIMMs x 2 NUMA nodes @ 2400MHz
NIC | Intel Corporation Ethernet Network Adapter X710-DA2 10Gbps
Microcode | 0x5003102
Intel NIC Device ID | 0x1572
Intel NIC Firmware version | 6.01 0x800035cf 1.1747.0
BIOS setting | CPU Power and Performance Policy <Performance> CPU C-state Disabled CPU P-state Disabled Intel(R) Hyper-Threading Tech Enabled Turbo Boost Disabled
Software
Operating System | CentOS Linux 7
Linux Kernel Version | 3.10.0-1160.31.1.el7.x86_64
GCC version | gcc version 4.8.5 20150623 (Red Hat 4.8.5-44)
DPDK version | 20.11
Traffic Generator : T-Rex

## Slide 8: What we learned
Benchmarking Results

## Slide 9: What we learned
Benchmarking Summary
  For packet loss measurement, results were not consistency at every tests trials
    T-Rex problem? Or other reason..
  The results of the NUMA-Affinity test were mostly similar to the expected values
    But in the small size packet, throughput was measured in terrible to use
Future Works
  Benchmarking results and trouble-shootings will be contributed to our draft
  Based on our full experiments of hackathon from IETF 106, plan to discuss with other related community (e.g., ViNePERF in Anuket) for improving BMWG work

## Slide 10: Wrap Up
Team members:
Younghan Kim (SSU)
KJ Sun (SSU)
Quang Huy Nguyen (SSU)
Jangwon Lee (SSU)
Hokeun Lim (SSU)
Minh Ngoc Tran (SSU)
Git repo:
https://github.com/huyng14/bmwg-container-networking
IETF Korea Forum:
Remote Hackathon Event at Busan
with I2NSF, IPWAVE (SKKU team)

## Slide 12: What we learned
Results
  SR/IOV has highest throughput, then
  VPP and OVS
  The gap between 3 techniques reduces
  as packet size increases
  SR-IOV has the most stable packet loss rate
  outperforms VPP and OVS
Explanation
  Reason 1
  Reason 2
  Reason 3
Accelaration Techniques Performance Comparison
  Throughput when increasing packet size

## Slide 13: What we learned
Results
  CNF & vSwitch on same NUMA
  has better throughput and packet
  loss rate than on different NUMAs
  NIC & vSwitch on same NUMA has
  better performance than on different
  NUMAs
Explanation
  Reason 1
  Reason 2
  …
NUMA effects on Accelaration Techniques
  Scenario 1: Single container on Single host

## Slide 14: What we learned
Test Results
NUMA effects on Accelaration Techniques
  Scenario 2: Multiple containers on Single host